## Slide 1
Autonomous BLE Attendance System
Zero External Hardware
Zero Manual Roll Calls
Tamper-Proof Social Mesh Graph

## Slide 2
The Problem: Traditional Attendance is Broken
01. Manual Roll Calls & Paper
• Wastes 3-5 minutes of lecture time in every class.
• Rampant 'proxy attendance' (calling out roll for an absent friend).
• Sign-in paper sheets get passed around, lost, or forged.
• Papers are tediusly hard to manage.
02. QR Codes & GPS Fencing
• QR codes can be instantly shared over WhatsApp.
• Students at home can scan the photo and get marked present.
• GPS does not work very well indoors .
• GPS margin of error (+/- 15m) cannot distinguish inside vs. outside corridor.
03. Biometrics & Hardware Beacons
• Fingerprint scanners form massive bottlenecks (queues of 60+ students).
• Facial recognition is slow, privacy-invasive, and fooled by high-res photos.
• ESP32 wall beacons require manual installation & battery maintenance.
• Hardware beacons can be stolen, unplugged, or physically cloned.

## Slide 3
Evolutionary Engineering: Lessons from Physical Radio Failures
Attempt 1: 2-Beacon Differential
Failed: The Doorway Trap
• Concept: Ratio between Teacher at podium and 1 child beacon at back wall.
• Physical Failure: Signal ratio (+10 dB) produced identical hyperbolic curves 1m inside and 1m outside the door.
• Conclusion: RSSI distance is scalar (no direction vector); cannot distinguish doorway spoofers.
Attempt 2: 3-Beacon Triangulation
Failed: Metal Resonant Cavity
• Concept: Elect 2 corner students to triangulate classroom bounds.
• Physical Failure: Concrete/metal reinforcement walls acted as RF waveguides. Back row received -70 dBm (reflections), middle got -82 dBm (body water absorption).
• Conclusion: Middle student was elected as farthest beacon every time!
Attempt 3: Pure BLE Multi-Hop Relay
Failed: Packet Clashes & Buffer Limits
• Concept: Offline students broadcast 20-byte relay vouchers over air.
• Physical Failure: Radio collision storm when 10+ students broadcast vouchers at once; 24-byte BLE payload limit; high packet loss.
• Conclusion: Discard active multi-hop relays; adopt pure cloud-audited in-degree graph witnessing.

## Slide 4
CORE ARCHITECTURE
Our Final Solution: Proximity vs. Transport Separation
JOB 1: PROXIMITY SENSING (BLE)
• Role: Pure local physical presence radar.
• Answers: 'Am I physically sitting 1 meter away from Student B?'
• Protocol: Low-power BLE whispers (< 2.5m range, median >= -85 dBm).
• Duration: Exactly 5 seconds at class start.
• Hardware: Standard smartphone BLE radio (Zero external hardware).
JOB 2: TRANSPORT & AUDIT (CLOUD API)
• Role: Secure data aggregation & mathematical proof audit.
• Answers: 'Does the reported topology form a legitimate cluster?'
• Protocol: Encrypted HTTPS REST endpoints via FastAPI.
• Speed: Audits 100+ students in under 15ms in cloud memory.
• Persistence: Permanent PostgreSQL records with roll number links.

## Slide 5
ALGORITHM
Social Mesh Graph Engine: Bilateral Affinity Scoring
Direct Mutual
1.00 Score
A ∈ P(B) and B ∈ P(A)
Both students reciprocally heard each other's 5s whisper. Proven physical desk neighbors.
Triadic Closure
0.50 Score
Shares ≥ 2 verified bridges
Student heard by 2 classmates who are already verified mutuals. Propagates presence across rows.
Peer Witness
0.85 Score
Witnessed by ≥ 2 verified peers
Offline students who could not send HTTP packets, but were heard by ≥ 2 verified classmates.
Hallway / Spoofer
0.00 Score
Unreciprocated link or 0 peers
Attacker claiming a student who never heard them, or isolated corridor spoofers. Flagged & rejected.

## Slide 6
SECURITY MODEL
3-Layer Security Architecture: Defense-in-Depth
JWT BEARER TOKENS
Layer 1: Cryptographic Digital Identity
• Proves: 'Who is holding this phone account?'
• Cryptographically signed with HS256 secret.
• Enforces strict role authorization (Teacher vs Student).
• Prevents submitting attendance under another student's ID.
DYNAMIC BLE NONCE (SALT)
Layer 2: In-Room Time-Synchronized Nonce
• Proves: 'Is this phone physically inside the classroom right now?'
• Teacher broadcasts ephemeral rolling salt over BLE (S:<SESSION>:<SALT>).
• Cannot be guessed by students at home.
• Backend checks salt; mismatches rejected as 'Nice try lil bro'.
LOW-POWER BLE WHISPERS
Layer 3: Physical Desk Proximity Mesh
• Proves: 'Are real classmates physically surrounding this phone?'
• Transmitted strictly at TX_POWER_LOW (-15 dBm, <= 2.5m fence).
• Walls cause >20 dB attenuation, eliminating corridor spoofers.
• Requires in-degree mutual witnessing in graph topology.

## Slide 7
OFFLINE SAFETY NET
Offline Capabilities: Autonomous Presence in Dead Zones
How a Student with Zero Internet / Data Plan is Verified Present
1. In-Room Radio Reception —
The offline student's phone receives the teacher's BLE beacon (S:89F2:9381) via direct radio waves (zero internet required).
2. Near-Field Whisper Probe —
The offline phone broadcasts its 8-byte whisper (89F2OFF1) at TX_POWER_LOW for 5 seconds.
3. Verified Online Neighbors Catch Probe —
Classmates to their left and right (who have cellular data) hear the probe at >= -85 dBm and add 'OFF1' to their Top-3 neighbors.
4. Pure In-Degree Cloud Audit —
The online neighbors submit their lists. The cloud graph engine observes: 'OFF1 submitted no HTTP report, but is witnessed by 2 verified classmates (ST01 and ST02)'. OFF1 is marked VERIFIED_PRESENT (0.85 affinity).
5. Single-Witness Safety Net —
If an offline student sits alone in a corner with only 1 online witness, they are marked ISOLATED_FLAGGED. The teacher confirms visually and verifies them in 1 tap.

## Slide 8
MOBILE CLIENT
Frontend Architecture: Native Android (Kotlin & Compose)
Strict Role Isolation
• Zero manual mode toggle.
• UI locks to Teacher or Student based on authenticated JWT claims.
• Teachers never scan; students never see teacher console.
BLE Hardware Layer
• BleAdvertiser: Low-latency service data advertising within 24-byte ceiling.
• BleScanner: Hardware UUID scan filter in LOW_LATENCY mode.
• Noise rejection filters ambient Bluetooth packets in 0ms.
Jetpack Compose UI
• Modern Material 3 reactive layout.
• Dual-mode Teacher Console: Broadcast Setup mode & Collapsible Audit Results.
• Student telemetry card with live dBm signal meters.
State Management
• AttendanceViewModel manages 5-state student machine (Standby -> Probing -> Verified).
• Auto session countdown & graceful HTTP error recovery.
• Live Compose snapshot reactivity.

## Slide 9
CLOUD BACKEND
Backend Architecture: High-Throughput Cloud Engine
FastAPI Async Engine
• Python 3.11 with ASGI asynchronous concurrency.
• Sub-15ms response latency under heavy classroom load.
• Clean modular routing (/auth, /attendance).
PostgreSQL on Neon
• Serverless PostgreSQL with auto-scaling compute.
• AsyncPG driver with PgBouncer pooling.
• 5 relational tables: Users, Courses, Sessions, Records, Staging Submissions.
Ephemeral Staging Table
• Multi-worker crash resilience.
• Check-ins staged in session_submissions DB table instead of volatile server RAM.
• Process-isolated across Uvicorn worker threads.
Single-Roundtrip Migration
• Atomic DO $$ BEGIN...END $$; block at application startup.
• Eliminates 35+ WAN roundtrips on cold start.
• Production-sanitized error handler prevents credential leakage.

## Slide 10
VERIFICATION
Optimizations, Testing & Key Milestones
Key Engineering Optimizations
• 5-Second Whisper Window: Reduced radio transmission time from 18.7s to 5.0s, reducing smartphone battery draw by 73%.
• Calibrated Proximity Threshold: Tuned median RSSI cutoff to -85 dBm for accurate classroom desk separation without hallway leakage.
• Automatic Session Supersede: Expired / abandoned sessions are auto-cancelled to eliminate teacher zombie lockouts.
• Auto-Logout on Expiration: Seamless 401 handling gracefully prompts for re-login with 1-year token persistence.
• Compose Snapshot Mutation Fix: Optimized peer map updates so RSSI meters and packet counters live-recompose instantly.
Rigorous Testing & E2E Simulation
• 100% Pytest Suite Passing: 12 comprehensive unit and integration test suites covering auth, graph algorithms, and security.
• 30-Student E2E Classroom Mesh Simulation: Simulated 25 online students, 4 offline students, and 1 hallway spoofer across 6 desk clusters.
• Simulation Result: Exactly 29 students verified (including all 4 offline students), 1 hallway spoofer rejected with 0.00 score.
• Anti-Cheat Verification: Verified that unreciprocated hallway links and invalid salt attempts are trapped and flagged on teacher screen.
• Android Build Success: Tested on physical Android devices and compiling cleanly under Gradle 8.7.

## Slide 11
PROJECT SUMMARY & VISION
Frictionless, Autonomous & Tamper-Proof
✓ Eliminates 100% of attendance roll call waste: Classes start in 5 seconds while phones rest in pockets.
✓ Zero hardware budget required: Runs solely on existing smartphones with standard Bluetooth Low Energy.
✓ Robust against fraud: Multi-layer security defeats buddy punchers, hallway proxies, and WhatsApp QR forwarders.
✓ Zero-configuration deployment: Works in any lecture hall without seating charts, room measurements, or calibration.
✓ Resilient offline safety net: Peer witnessing ensures students in basement halls never lose attendance credits.